## Slide 1: NeurIPS 2020 L2RPN Robustness and Adaptability Tracks Competition Winning Approach
YANG Zhihong, XU Chunlei, LU Jixiang*, XU Hongsheng, XU Kang,
CHEN Tianyu, XU Zhilin, LIU Junjun, LU Jinjun, CHEN Tianhua
(* Corresponding author)

## Slide 2: Track1 ：Robustness Track
Methodology
Tricks
Results
Problem description
Goal: Develop agent to be robust to unexpected events and keep delivering reliable electricity everywhere even in difficult circumstances.
Operation Cost: Operate the grid as long as possible, minimize the operation cost including powerlines losses, redispatch cost and blackout cost (penalty).
An adversarial opponent will attack some lines of the grid everyday randomly.

## Slide 3: Track2：Adaptability Track
Methodology
Tricks
Results
Problem description
Goal: Develop agent to adapt to new energy productions in the grid with an increasing share of renewable energies which might be less controllable.
Operation Cost: Operate the grid for as long as possible, minimize the operation cost including powerlines losses, redispatch cost and blackout cost (penalty).
Renewable energies varying from 1x to 3x

## Slide 4: Rules and Score
Methodology
Tricks
Results
Problem description
tend
Te
N
t 1
t tend
i1
Rules and Constraints
Demand-supply balance should be met at any time without load shedding.
Tripping power plant is not allowed.
Electrical islands are not allowed.
Any action has a certain cool down time.
…
Score
The agent with less blackouts and less operation costs will be given higher score.
Coperations (t)  Closs (t)  Credispatching (t) Cblackout (t)  Load (t)*  * p(t),   1
C(e)   Coperations (t)   Cblackout (t)
Score   C(ei )

## Slide 5: Action
Methodology
Tricks
Results
Problem description
Generation redispatch action: modifying the production set point with redispatching
Substation Topological action: switching busbar connection between double busbars for each substation object.
Powerline Status action: reconnecting / disconnecting a power line
Do-Nothing action

## Slide 6: State
Methodology
Tricks
Results
Problem description
State chosen:
Some states (such as prod_p, load_p, topology_vect, time_next_maintenance, line_status, rho etc.) are necessary in our action selecting process.
Inherent properties in power grid (e.g thermal_limit of lines) and some properties of generators (e.g max_ramp_up)
etc.)
which
State unchosen:
Another part of states (such as date, time, prod_q, load_q
have no contribution to our action selecting process.

## Slide 7: Dual-agent strategy
Methodology
Tricks
Results
Problem description
Do nothing
Operate normally?
Action
Y
N
Emergency?
Base Agent
DRL
Agent
Prioritized Replay Buffer
ENV
N
Y
Update Agent
Sampled batch
Selected emergent transition sample (s,a,r,s´)
Grid state
(Load & generator fluctuation, Attack& maintenance)
State Update
Base Agent: Based on prior knowledge and simulation result, handling some relatively easy-to- solve situations if grid operates abnormally.
DRL Agent: Based on Dueling-Double-DQN, handling complicated situations if base agent can’t.
*Inspired by the works of Ziming Yan, Yan Xu, Nanyang Technological University
(https://github.com/ZM-Learn/L2RPN_WCCI_a_Solution)

## Slide 8: Base-agent strategy
Any overflow?
Line get disconnected
Problem causes: 1.cyber-attacks 2.Hazards 3.Maintenance 4.Load
fluctuations
Overflow time>3?
Do Nothing
Y
Y
N
N
N
Line disconn ected?
Line Reconnect
Topo/Redisp/LineDisc
Y
Methodology
Tricks
Results
Problem description

## Slide 9: DRL agent
Methodology
Tricks
Results
Problem description
We adopt the Dueling-Double-DQN(D3QN) algorithm for our DRL agent, a kind of value based algorithm which can handle discrete action-space problems.
V(s)
A(s,a)
D3QN Neural network structure diagram
Robustness Track: State size=744，Action size=885 Adaptability Track: State size =2300，Action size =1164
Q(s,a)
=A(s,a)+V(s)
State

## Slide 10: Rewards
Methodology
Tricks
Results
Problem description
Adaptability Track （Track2）
Sandbox-Reward
Close-To-OverFlow-Reward
Distance-Reward
Lines-Capacity-Reward
Robustness Track （Track1)
Sandbox-Reward
Close-To-OverFlow-Reward
Distance-Reward
Rewards: (factors considering)
Sandbox - economic
Close-To-OverFlow - overflow
Distance - difference with initial topology 4.Line-capacity – available transfer capacity
Reward=∑Weight(i)*Reward(i),i∈(Sandbox, CloseToOverflow, Distance, LineCapacity)

## Slide 11: Reduced Action-space
Methodology
Tricks
Problem description
Robustness Track（Track1)
Results
Why action-space need to be reduced?
Adaptability Track （Track2)
The topology action number is huge due to complex action combination.
Difficult for system simulation and agent training.
We reduce them according to domain knowledge and experiments.
Before reduce: 130k (2^17 = 131,072)
After reduce: 885
58 line, 786 topo, 40 redisp, 1 donothing
Before reduce: even more!
After reduce: 1164
185 line, 978 topo, 1 donothing

## Slide 12: Guided exploration
Methodology
Tricks
Results
Problem description
Epsilon-greedy exploration
State
DNN
Q1 Q2
Qn
Q_highest Q_2nd
Q_lowest
sort
Large Action-space
Long MDP chain
Local optimum
Stable
Better experience
Efficient
Guided exploration
Score_highest Score_2nd
Score_lowest
Pick top5 Q- value, Simulate
and sort
Q_highest Q_2nd
Q_lowest
…

## Slide 13: Results
Results
Problem description
Methodology
Tricks
50-year simulated training data and 24-week test data for each competition track.
Blue indicates scenarios passed, orange indicates scenarios black-out.
We will optimize our agent for the failed cases in future work.
Robustness Track Test Result
Adaptability Track Test Result

## Slide 14: Results
Methodology
Problem description
Robustness Track:
Tricks
Adaptability Track:
Results
We are one of top performers in both NeurIPS Robustness Track and Adaptability Track competitions.
1.rl_agent team is the best team with a score of 25.53 2.kunjieTang team ranks 2nd with a score of 24.66
3.lujixiang team ranks 3rd with a score of 24.63
1.rl_agent team is the best team with a score of 59.26 2.binbinChen team ranks 2nd with a score of 46.89
3.lujixiang team ranks 3rd with a score of 44.62

## Slide 15: Thanks！